## Slide 1: CFET defines the future of control system
Control system Framework Experimental Toolkit
Control system For EveryThing

## Slide 2: Re Cap

## Slide 3: The Most Important Aspect: Interoperability
Many effort seems been put into it. But little have been achieved.
Everybody wants to dominate.
Does not means using the same protocol.

## Slide 4: The current IoT approach is wrong
There is no good to give everything an IP address
  6Lowpan is limited and meanless
The current protocol are just lies
  MQTT is a liar: heavy, needs broker, designed to sell services
  CoAP is a joke: like RESTful by not and not compatible and not light
Implementing the above is expensive!
The most popular solution out there is nRF24L, ESP8266
$1
$15

## Slide 5: Modeling of things
Status
  Read by others changed by self,
  by looking at the statuses solely, one can determine all the output and behavior of the thing.
Configuration
  Read by self changed by others,
  Represent the desired behavior
Method
  A command
  Event handler

## Slide 6: Modeling of things
Resource
  Status
  Config
  Method
  Interoperate means: Locate and access resources

## Slide 7: Modeling of things
World
  Unlimited interoperability is bad

## Slide 8: Modeling of things
What is a thing?
  Has resources
  Can be physical or virtual
  Things can aggregate into bigger things

## Slide 9: Dumb and Smart Things
Cost!!!!
Dumb thing is god damn cheap!!!
But still interoperable
How?

## Slide 10: Dumb and Smart Things

## Slide 11: Dumb Protocol Pattern
Language
Identity
Knowledge
Existing protocol can be parsed in the above way

## Slide 12: Dumb Protocol Pattern
Bindings:
  Static:
    The avatar it preconfigure and knows the identity of the dumb things, and have the knowledge of the resource on the dumb things.
  Interactive
    The avatar is not preconfigured. But when the dumb thing request a bind the avatar is created and the smart device can be recognized the dumb device and then establish the knowledge from pre-configurations or looking up a knowledge base but not from the dumb thing.
  Dynamic
    The avatar is not preconfigured. When the dumb thing request a bind the avatar the avatar is created and the smart device cannot be recognized. The smart thing cannot establish the knowledge base. It then negotiate with the dumb thing to establish the knowledge.

## Slide 13: Web of things
Already lots of things connected to the internet but interoperability is not achieved
But the web is an exception
The fundamental of web is HTTP and HTML. We will leverage on these.
Web is also in massive scale

## Slide 14: Web of things
RESTful
  Resource located by URI.
  Access indicated by verb
  Hypermedia!!!
    Using JSON-LD
    Embrace the semantic web
HTML JS
  HMI auto generation

## Slide 15: Implementation
Smart things

## Slide 16: CFET is a mediator

## Slide 17: Let’s dig deeper

## Slide 18: Overall view of CFET2 internals
Agent/Proxy

## Slide 19: CFET2Module
Objects that consume CFET2 services
They access the CFET2 service from Hub
Thing
  User implemented functions
  Expose methods and properties resources
CFET2Host
  The CFET2Module with highest privilege
  Add things to the Hub
Communication Module
  Like Hub for remote access
Pipeline
  Process the sample returned by resources before t get to the requester

## Slide 20: Resource
What is a resource?
  It is a internal agent object that CFET2 used to manage access to the real properties and methods in the Things.
ResourceBase
ResourceThing
ResourceConfig
ResourceStatus
ResourceMethod

## Slide 21: ResourceBase
Name
Path
  The mount point + the name
IsOriginal
  Reserved for future
ResourceType
  Abstract, Thing, Status, Config, Method
Get
  All types of resources support get

## Slide 22: ResourceStatus
The single most important resource
PropertyGet
  implementations
MethodGet
  implementations
ParentResource
  This is point to a ResourceThing
AddImplementation
  Get: Property, Method with return value
Get
  Array input
  Dictionary input

## Slide 23: ResourceConfig:ResourceStatus
PropertySet, MethodSet
Config Will also support insert, delete,
AddImplementation:
  Set: Property with setter, method with at least one input parameter
  Get: Property with getter, method with return value
  GetSet(default): Property with getter and getter

## Slide 24: ResourceMethod : ResourceStatus
AddImplementation:
  Get: return invalid sample, this will be replace by a method info object
  Invoke: any method

## Slide 25: ResourceThing:ResourceBase
TheThing
  Keeps a ref for the Thing it represents
Dictionary<string, ResourceBase> Resources
  Contains all resources
ProbeTheThing
Get: returns invalid, but will return the thing detail

## Slide 26: Sample
Sample are the response when you access a resource!
Why sample?
  Return more then the resource value such as metadata, hypermedia etc.
  Pipeline can modify the sample add more info
ISample
SampleBase
Config
Status
Method

## Slide 27: ISample
object ObjectVal { get; }
TVal GetVal<TVal>();
bool IsValid{get; }
Dictionary<string, object> Context { get; } //Very importnat!!!
ISample AddErrorMessage(string msg);
string Path { get; }
ISample SetPath(string path);

## Slide 28: Hub
Hub
  It is a avatar of a HubMaster
  For security reason
HubMaster
  Singleton!

## Slide 29: Hub
You can not new a Hub, it is injected to by inherit from CFET2Module
Pipeline, not correctly implemented by Chen Ming
EventHub, a hub for event, more on it later
TryAddThing
TryAddCommunicationModule
StartThings
StartCommunication

## Slide 30: Hub
TryAccessResourceSampleWithUri(ResourceRequest request)
ResourceRequest(Hub hub, string uri,AccessAction action, object[] inputarray, Dictionary<string, object> inputdict, Dictionary<string, string> extraRequest, bool usingdict = false)
TryGetResourceSampleWithUri(string requestUri, params object[] inputs)
TryGetResourceSampleWithUri(string requestUri, Dictionary<string,object> inputDict)

## Slide 31: URI
How URI is convert to thing path and parameters ??!!

## Slide 32: Thing
TryInit(object initObj) //called when add to hub
virtual void Start() //called when hub.StartThings() is called, which is after all the things are added thus inited.
public string Path { get; internal set; }
public string GetPathFor(string resourceName)
{
return Path + @"/" + resourceName;
}

## Slide 33: Event
Look for the document its very clear!

## Slide 34: How to make a thing
Inherit from Thing
Cfet2ConfigAttribute
Cfet2MethodAttribute
Cfet2StatusAttribute
Then consume Hub and Hub.EventHub and Log
Example

## Slide 35: CFET2APP
Config Log Provider
New a host
Add Thing
Add Communication
Start Commnication
Start Things
Listen to CLI